## Slide 1: Statutory Requirements
Design
Installation &
Commissioning
Maintenance &
Repair
Modernisation
Replacement
Design

## Slide 2: Statutory Requirements
Design
  Lifts Regulations 1997
  The Supply of Machinery (Safety) Regulations 2008
  Building Regulations (Scotland-Tech Handbook & England Part M)
  Construction (Design and Management) Regulations 2007
  BS 5655-6:2002 Code for the selection and installation of new lifts
  BS 9999:2008 Code of practice for fire safety
  BS ISO 4190 Lift Classifications
  BS EN 81 Series of Standards - 1, 2, 28, 70, 71, 72, 73
  BS EN 115-1:2008 +A1 2010 - Safety of escalators and moving walks - Construction and installation
Notes: Highlight that hand-outs will be provided and this will list the relevant legislation and standards which are covered in the presentation

## Slide 3: Statutory Requirements
Design
  How do you know whether the lifts you own or manage are suitable for the buildings and the users that work or live there?
  How many lifts are required? Who will use them? What will they be used for?
Notes: Highlight that there is legal obligation to ensure that the lifts/escalators and buildings which we manage and operate need to be safe and fit for purpose. The type of user, building and environment may all impact on the safety of the equipment.

## Slide 4: Statutory Requirements
Design
  How does design and the law affect me?
Notes: Highlight that designers, importers, manufacturers and suppliers all have a statutory obligation to ensure the safety of the equipment which they design or supply. Reasonably steps must be taken to understand how the equipment will be used and its intended application.

## Slide 5: Statutory Requirements
Design
  Legislation, EU & British Standards protect you against
  Products which are not fit for purpose or the intended application
  Lifts which pose a hazard to the users
  Lift shafts and machinery spaces, which contain hazards
  Unsafe working conditions for maintenance personnel
  Inaccessible equipment which can’t be properly used or maintained
  Lifts which are not accessible to all users
  Inadequate fire safety and evacuation provision
  Design according to Legislation, Standards and Best Practice and check that equipment will be suitable for the building, users and the intended application.
Notes: Summary

## Slide 6: Statutory Requirements
Design
  Legislation and standards can protect you against accidents which result from poor design co-ordination and a lack of knowledge of the user, building and application.
Glass infill
No access to stop button
Notes: Highlight that design co-ordination and co-operation with others involved in the process can avoid unforeseen risks from arising at a later stage.

## Slide 7: Statutory Requirements
Installation &
Commissioning
  The Lifts Regulations 1997
  The Supply of Machinery (Safety) Regulations 2008
  Construction (Design and Management) Regulations 2007
  The Management of Health and Safety at Work Regulations 1999
  BS 8486: 2007 Examination & Test of New Lifts
  BS 6440: 2011 Powered Vertical Lifting Platforms
  BS EN 81 Series of Standards - 1, 2, 28, 70, 71, 72, 73.
  BS EN 115-1:2008 +A1 2010 - Safety of escalators and moving walks - Construction and installation

## Slide 8: Statutory Requirements
Installation &
Commissioning
  OK…so now my lift has been designed properly how do I ensure it will be installed and commissioned properly?
  Careful planning and co-ordination of the construction team
  A clear understanding of the construction site risks and processes
  Realistic programme timescales which allow sufficient time for the installation
  Specified installation quality standards
  Explicit testing and commissioning procedures
  Final validation or witness testing by a competent person

## Slide 9: Statutory Requirements
Installation &
Commissioning
Fire Alarm
  Careful planning and co-ordination of the construction team
Hoarding preventing access to alarm
  A clear understanding of the construction site risks and processes
Notes: Highlight that it is essential to understanding the risks associated with construction sites to allow effective co-ordination and to avoid simple hazards which could otherwise be avoided. MHSWR and CDM regs place and obligation on clients to ensure that correct procedures are in place to ensure the safety of employees and members of the public.

## Slide 10: Statutory Requirements
Installation &
Commissioning
  Realistic programme timescales which allow sufficient time for the installation
Opening tomorrow at 9am

## Slide 11: Statutory Requirements
Installation &
Commissioning
  Well in that case here is your lift, all tested and ready to go
Notes: Planning, organising, control and monitoring are fundamental requirements of any health and safety management system and each element requires the necessary resources to be effective. Highlight that there’s no point in setting unrealistic goals which are not achievable and pose additional risk to those responsible for delivering the end service or product and ultimately the user.

## Slide 12: Statutory Requirements
Installation &
Commissioning
  Explicit testing and commissioning procedures

## Slide 13: Statutory Requirements
Installation &
Commissioning
  Final validation and certification to demonstrate legislative compliance

## Slide 14: Statutory Requirements
Installation &
Commissioning
  CE marks should be displayed once all the other testing and commissioning procedures have been completed and the lift complies fully with current legislation

## Slide 15: Statutory Requirements
Installation &
Commissioning
  OK…so now my lift has been designed properly how do I ensure it will be installed and commissioned properly?
  Careful planning and co-ordination of the construction team
  A clear understanding of the construction site risks and processes
  Realistic programme timescales which allow sufficient time for the installation
  Specified installation quality standards
  Explicit testing and commissioning procedures
  Final validation or witness testing by a competent person

## Slide 16: Statutory Requirements
Maintenance &
Repair
The Management of Health and Safety at Work Regulations 1999
  Lifting Operations and Lifting Equipment Regulations (LOLER) 1998
  Provision of Use of Work Equipment Regulations (PUWER) 1998
  The Control of Substances Hazardous to Health Regulations (COSHH) 2002
  BS EN 13015 2001 - Maintenance for lifts and escalators - Rules for maintenance instructions
  BS 7255 Code of practice for Safe Working on Lifts 2001
  SAFed Guidelines on the supplementary tests of in-service lifts 2006

## Slide 17: Statutory Requirements
Maintenance &
Repair
  How can I be sure that maintenance work is being carried out properly and what certification do I need?
  Valid and current insurance surveyors reports (LOLER)
  Up to date maintenance reports and log card records
  Maintenance procedures which reflect the specific needs of the lift/escalator
  A process which ensures that recommendations from your insurer/contractor are given full consideration
  Maintenance quality auditing processes and management procedures which ensure statutory and contractual compliance

## Slide 18: Statutory Requirements
Maintenance &
Repair
  How can I be sure that maintenance work is being carried out properly and what certification do I need?

## Slide 19: Statutory Requirements
Deign
Modernisation
  BS 5655-11/12 2005 - Code of practice for the undertaking of modifications to existing electric/hydraulic lifts
  BS EN 81-80 2003 Rules for the improvement of safety of existing passenger and goods passenger lifts
  BS EN 115-2 - 2010 - Rules for the improvement of safety of existing escalators and moving walks
  DD CEN TS 81-82 2008 Improvement of the accessibility of existing lifts for persons including persons with disability
  DD CEN TS 81-83 2009 Rules for the improvement of the resistance against vandalism

## Slide 20: Statutory Requirements
Deign
Modernisation
  How do I prioritise what to do?
  How do I ensure that any modernisation work does not compromise the safety of my lift/escalator?
  When undertaking modifications to an existing lift/escalator the first consideration should be the retention of at least the existing level of safety. Under no circumstances should the installation be less safe after the modifications have been made.

## Slide 21: Statutory Requirements
Deign
Modernisation
  How do I prioritise what to do?

## Slide 22: Statutory Requirements
Deign
Modernisation
  How do I ensure that any modernisation work does not compromise the safety of my lift/escalator?

## Slide 23: Statutory Requirements
Deign
Modernisation
  Example – you decide to replace the lift car interior only.
  After
  Steel wall panels
  New ceiling
  New lighting
  Stone floor
  Before

## Slide 24: Statutory Requirements
Deign
Modernisation
  If all I have done is to replace the lift car interior fittings and fixtures do I still need to follow all of the above legislation/standards?
  What are the consequences/risks associated with this modification?
  Increased lift car mass/weight
  Will the lift machine be able to lift the load and will the building support it?
  Will the lift car frame be strong enough?
  Will the ropes/suspension system still be sufficient?
  Will the buffers, safety gear and guide rails still be suitable if all else fails?

## Slide 25: Statutory Requirements
Deign
Modernisation
  How do I prioritise what to do?
  How do I ensure that any modernisation work does not compromise the safety of my lift/escalator?
  BS EN 81-80 Risk Assessment
  BS 5655-11/12 2005 - Code of practice for the undertaking of modifications to existing electric/hydraulic lifts
  Ensure that the formulation or specification of any modernisation scheme is done in conjunction with a competent person with sufficient experience and knowledge to undertake a risk assessment to identify any issues which need to be addressed to ensure the safety of the modified installation.
  Final testing and commissioning procedures to demonstrate compliance

## Slide 26: Statutory Requirements
Replacement
  BS EN 81-21 2009 New passenger and goods passenger lifts in existing building
  BS EN 81 Series of Standards - 1, 2, 28, 70, 71, 72, 73.
  BS EN 115-1:2008 +A1 2010 - Safety of escalators and moving walks - Construction and installation
  Lifts Regulations 1997
  The Supply of Machinery (Safety) Regulations 2008
  Building Regulations (Scotland-Tech Handbook & England Part M)

## Slide 27: Statutory Requirements
Replacement
  Is there anything else I need to consider over and above the lift?
  Is the existing power supply sufficient?

## Slide 28: Statutory Requirements
Replacement
  Is there anything else I need to consider over and above the lift?
  Access to machinery spaces

## Slide 29: Statutory Requirements
Replacement
  Is there anything else I need to consider over and above the lift?
  Reduced pit depth and head room safety spaces

## Slide 30: Statutory Requirements
Replacement
  Is there anything else I need to consider over and above the lift?
  Asbestos

## Slide 31: Statutory Requirements
Replacement
  Is there anything else I need to consider over and above the lift?
  Non lift services, water, gas, electricity, telecom etc.

## Slide 32: Statutory Requirements
Replacement
  When I’ve dealt with all the other issues how do I ensure that the new lift will comply with legislation and standards?
  Commissioning procedures & tests
  Declaration of conformity
  CE Mark
  Final validation by competent person
  Remember by complying with legislation and following standards, guidance and best practice you are protecting the safety of yourself, your colleagues and members of the public.